## Slide 1: CVD and dielectric films lecture review
Notes compiled 4/9/20, Sean Lai

## Slide 2: Thin film + Deposition characteristics
THIN FILMS:
Not fully dense, defects different from bulk
Under stress  deformation due to CTE difference between film and SiO2
Quasi-2D
Characterized by surface + interface effects
  DEPOSTION:
  Emmision  transport  condensation
  Types: CVD, PVD, others (e.g. spin coating)
  Characteristics:
    Deposition rate
    Uniformity
    Material types
    Quality
    Directionality
    Cost

## Slide 3: Growth Characteristics
Conformal vs. Nonconformal (step coverage)
  Non conformal  difficulty with trences and void creation
Equilibrium Growth:
  2D (van der Merwe): epitaxial, high temp, slow
  3D (Volmer-Weber): Islands
  2D  3D (Stranski-Krastanov): layers then islands
  Latter two are polycrystalline or amorphous
Mode Parameters:
  Lattice mismatch
  Supersaturation
  Gibbs FE  Wetting

## Slide 4: CVD Process
STEPS:
Reactants  Surface
Migration on Surface
Reaction at Surface
Nucleation  Islands  Uniform film
REACTION PROCESS:
Bulk transport
Gas-phase reactions
Transport to surface
Adsorption at surface
Surface reactions  Nucleation
Desorption of byproducts
Transport of byproducts from surface

## Slide 5: Reactor Types
APCVD:
760 torr
Ni buffer zones
Controlled by temperature, flowrate, belt speed(~time)
LPCVD:
0.1-1 torr
High temp  > 650°C
Controlled by wafer temperature
PECVD:
1-10 torr
Increased reaction rate due to ionization
High deposition rate at low temperature
HDPCVD:
Low temperature (150°C)
Low pressure (1-10 mTorr)
400°C by bombardment
Simultaneous deposition/sputtering

## Slide 6: Dielectric CVD Parameters
CONFORMITY/STEP COVERAGE:
Better at low pressure or high mobility
CHEMISORPTION VS. PHYSISORPTION:
Chem: high bond energy, low mobility
  Used for SiH4, silicon source
Phys: low bond energy, high mobility
  TEOS, oxide source
REACTION PARAMETERS:
Surface-reaction limited  slow rate, temperature sensitive
Mass-transport limited  high rate, mass flow controlled
APPLICATIONS:
STI (shallow trench isolation): isolation between transistors
ILD (inter dielectric layer): insulation between interconnects
Passivation: IC protection from moisture or mechanical damage

## Slide 7: Questions + Conclusions
CVD integral to semiconductor manufacture
Balance of input parameters to achieve different outcomes
Geometry of etching important to film characteristics
Some parallels with graphene: e.g. lattice matching, gibbs FE.
Low temperatures (<400°C ?) needed to prevent damage to FETs
Is annealing effective for non-metallic thin films?
How does CTE effect graphene growth  wrinkles?